## Slide 1: Revolutionizing Turbine Cooling with Micro-Architectures Enabled by Direct Metal Laser Sintering
The Ohio State University
Aerospace Research Center
J.P. Bons, A. Ameri, J. Gregory,
M. A. Hossain, E. Asar
(6 Nov 2019 – NETL UTSR Workshop)

## Slide 2: Research Team
TEAM LEAD
Dr. Jeffrey Bons
Focus: Experimental Fluid Mechanics and Heat Transfer
Co-PI
Dr. Ali Ameri
Focus: Computational Fluid Dynamics and Heat Transfer
Co-PI
Dr. Jim Gregory
Focus: Experimental Fluid Mechanics, Fluidic Oscillator Development
Arif Hossain
PhD Candidate
Elif Asar
MS
Robin Prenter
PhD
Ryan Lundgreen
Postdoc
Lucas Agricola
MS
Contributing Students and Researcher

## Slide 3: Objectives
Explore innovative cooling architectures enabled by additive manufacturing techniques for improved cooling performance and reduced coolant waste.
Leverage DMLS to better distribute coolant through microchannels, as well as to integrate inherently unstable flow devices to enhance internal and external heat transfer.
Demonstrate these technologies
  at large scale and low speed.
  at relevant Mach numbers in a high-speed cascade.
  finally, at high speed and high temperature.
Complement experiments with CFD modeling to explore a broader design space and extrapolate to more complex operating conditions.

## Slide 4: Integration of Promising Designs in NGV
1. Reverse Cooling on PS:
Fed by upstream microchannel
Better surface coverage with lower massflow?
3. Sweeping Jet Impingement Cooling on LE:
Eliminate showerhead
Lower massflow required?
Microchannel exhaust
4. Microchannels in TE:
Improved coverage with lower massflow required?
Weight savings with skin cooling?
2. Sweeping Jet Film Cooling on SS:
Improved coverage with lower massflow required?
1
2
3
4
Sweeping jet film cooling
Microchannel and Micro-architecture
pin-fin cooling

## Slide 5: Turbine Heat Transfer Facilities
For innovative concepts to be viable, must be vetted in facilities that simulate the real operating environment
Graduated complexity -
  High speed
  Engine scale
  High temp (Tw/Tb)
  Low speed
  large scale
  Low temperature
  High speed
  Smaller scale
  Low temperature
Phase 1
Phase 2
Phase 3

## Slide 6: Assessment of Innovative Cooling Concept
Best cooling concepts were qualified for the next phase.
Test Facility | Flat plate | Low-speed cascade | High-speed cascade | High-temperature cascade
1. Reverse cooling |  |  |  | 
2. Sweeping jet film cooling |  |  |  | 
3. Sweeping jet impingement cooling |  |  |  | 
4. Micro-channel cooling |  |  |  | 
5. Micro-architecture pin-fin cooling |  |  |  | 
Flat plate
Large scale
Low-speed
cascade
High-speed
cascade
High temperature
cascade

## Slide 7: Assessment of Reverse Film Cooling
PIV
LES
Flow field was experimentally characterized using flow visualization, PIV and thermal field measurements.
Conventional
Reverse
Conventional
Reverse
Heat transfer augmentation
Cooling Effectiveness
Net heat flux reduction
Reverse cylindrical film cooling produces a high, laterally uniform adiabatic cooling effectiveness
Reverse cooling was outperformed by the conventional film cooling due to high heat transfer augmentation.
*Select applications based on geometry/design

## Slide 8: Assessment of Sweeping Jet Film Cooling
Flat plate
NGV(subsonic)
NGV(transonic)
Fluidic Oscillator

## Slide 9: Assessment of Sweeping Jet Film Cooling
Sweeping jet hole shows higher lateral cooling effectiveness compared to shaped hole at all design conditions.
The sweeping motion of the jet prevents the formation of CRVP and promotes lateral spreading of coolant that improves the near hole cooling effectiveness.
The pressure loss across the sweeping jet hole and the aerodynamic loss are comparable to the standard shaped hole.
The averaged cooling effectiveness () for the sweeping jet hole improves at high blowing ratio (M>1).
Flat plate
NGV(subsonic)
NGV(transonic)
Flat plate
NGV
SJ hole
777- hole
SJ hole
777- hole
SJ hole
777- hole
SJ hole
777- hole
SJ hole
777- hole

## Slide 10: Assessment of Sweeping jet Impingement
A matched Bi-number approach was adopted to estimate the overall cooling effectiveness.
Although the local heat transfer for steady jet dominates, the cooling uniformity for Sweeping jet is much higher than the steady jet.
Overall cooling effectiveness
Large scale test piece
NGV(subsonic)

## Slide 11: Assessment of Microchannel Cooling
Microchannels, ribbed turbulators, and pin arrays were comparatively analyzed for heat transfer and pressure drop.
Application for trailing edge cooling.
Concept is to keep the coolant near the wall to reduce coolant massflow requirement
The microchannel array drops far more pressure than the other designs.
Pressure drop

## Slide 12: Assessment of Pin-Fin Cooling
Since microchannels did not show promise due to high pressure drop, focus was given to develop innovative pin-fin design.
Experimental Setup
Cylindrical pin-fin
Triangular pin-fin
Single-walled
Double-walled
Single-walled
Double-walled
Wall thickness = 0.75mm

## Slide 13
Overall Cooling Effectiveness
Assessment of Pin-Fin Cooling
The triangular pin-fin with clearance and impingement jet (double-walled) showed the highest cooling effectiveness.
Coolant Massflow
Cylindrical pin-fin (PF)
Triangular pin-fin (TF)
PF with jet (PFC jet)
TF with jet (TFC jet)

## Slide 14
Per pixel temperature prediction
Heat Transfer Coefficient
Assessment of Pin-Fin Cooling
A 1-D transient lumped (0.75mm wall thickness) capacitance method was used for each image pixel to predict the wall temperature distribution for a guessed internal HTC.
Convergence
Nu
Neglecting lateral conduction within the wall, the 1-D lumped thermal capacitance method (Nirmalan et. al., 2003) can be represented as-
The predicted wall temperature distribution () is then compared with the measured wall temperature distribution.
An iterative method was adopted to update a new HTC to predict a new wall temperature.
The error between the predicted and measured wall temperature was kept below 0.05%.
Transient
IR data

## Slide 15
Heat Transfer Coefficient
Assessment of Pin-Fin Cooling
A transient IR measurement was performed assuming a suddenly heated plate configuration to estimate the convective heat transfer coefficient.
The double-walled configuration showed higher heat transfer compared to the single walled configuration.
Cylindrical pin-fin (PF)
Triangular pin-fin (TF)
PF with jet (PFC)
TF with jet (TFC)
Coolant Massflow

## Slide 16
Pressure Drop Measurement
Assessment of Pin-Fin Cooling
The full length triangular pin-fin (TF) shows the maximum pressure drop.
The partial length triangular pin-fin can still provide a better heat transfer (higher overall cooling effectiveness) with a comparable pressure drop.

## Slide 17
Internal Flowfield (CFD)
Assessment of Pin-Fin Cooling
Computational Grid
The triangular pins show the formation of a pair of counter rotating streamwise vortices.
The pin-fin prevents the strong crossflow, as the coolant jet impinges and moves farther downstream.
The triangular pin wall redirects the coolant in the spanwise direction thus augmenting local heat transfer and improving cooling effectiveness
Q-criterion colored by streamwise vorticity
PF
TFC
No pin

## Slide 18: PHASE 3: Fully Simulated NGV
Fabricate high-temperature alloy vane using DMLS
Characterize surface roughness and tolerances due to manufacturing method
Test full material system in the TuRFR turbine test facility
  Characterize cooling performance and pressure drop at various coolant mass flow rates
  Characterize cooling performance at various main flow conditions
Compare new vane design performance to conventional vane at same coolant and main flow operating conditions to determine improvement
Develop computational model of NGV
  Generate and validate flow solution in context of TuRFR testing
  Generate simulations at higher temperatures and pressures not possible in the facility

## Slide 19
DMLS Scale Assessment
Build direction Assessment
Scale Comparison
Four fluidic oscillators (DMLS – Inconel 718) have been characterized.
Two separate designs (FOFC and FOIC) with two different build directions were studied. (Dh = 1.1mm)
The characterization was performed by measuring the oscillation frequency and visualizing the jet spreading by water flow visualization.

## Slide 20
DMLS Scale Assessment
Only FOIC 2 showed a strong jet oscillation.
Severe blockage at the inlet (FOFC 1 and FOFC 2) section was observed which is believed to be responsible for the deteriorating performance.
The oscillators were scaled 30% larger
(Dh = 1.4mm) for the final design.

## Slide 21
DMLS Vane Design
Adiabatic Wall Temperature (Uncooled)
GEnx doublet
Pressure distribution
Temperature distribution
Computational
domain
A set of CFD calculation has been performed to estimate the adiabatic wall temperature
= 1375K (2000F)
Pressure ratio:
The wall temperature was used to determine the film hole location

## Slide 22
Conjugate Heat Transfer (CFD)
DMLS Vane Design
Overall Cooling Effectiveness
Computational
domain
Material: Inconel 718. Wall thickness: 1.5mm
Flow condition:
  Pressure ratio: ,
  = 1375K (2000F)
  = 850K (1070F)
Steady state calculation with hybrid grid.

## Slide 23
DMLS Vane Design
Two separate vane geometries were designed using OSU vane profile
Vane with
advanced cooling
Baseline vane with
conventional cooling
Sweeping jet film cooling on SS
Sweeping jet impingement cooling at the LE
Double walled triangular pin-fin cooling at the TE
777-shaped film cooling on SS
Circular jet impingement cooling at the LE
Single walled cylindrical pin-fin cooling at the TE

## Slide 24
DMLS Vane Design
Two rows of cylindrical gill shaped at the LE.
Two additional rows of holes at the SS and PS.
Parameter | Value
Chord | 76mm
Span | 65mm
Solidity | 1.45
Aspect ratio | 0.85
SJ/777Film hole diameter | 1.4mm
Cylindrical hole diameter | 1.1mm
Cylindrical pin dia | 1.5mm
Pin (S/D, X/D) | 2.5mm
Pin-fin jet diameter | 1mm
Geometric detail
Advanced vane
(SJ vane)
Baseline vane
(777-vane)

## Slide 25
DMLS Vane Design
Print Description
Parameter | Value
DMLS Material | Inconel-718
Minimum Layer thickness | 30
Build direction | Compound
Minimum feature size | 0.318mm
Part tolerance | 0.0760mm
Surface roughness | Ra = 5-10
Parameter | Value
DMLS Material | Inconel-718
Minimum Layer thickness | 
Build direction | Compound
Minimum feature size | 0.318mm
Part tolerance | 0.0760mm
Surface roughness | 
Singlet Assembly
SJ-vane
777-vane
Dummy vane

## Slide 26
DMLS Vane Design
Device Characterization
Water Flow Visualization
Oscillation frequency was measured for each hole.
Similar peak oscillation frequency was observed for each hole.
Water flow visualization confirmed that each hole is oscillating at a very similar jet spreading.
Peak frequency

## Slide 27
Turbine Reacting Flow Rig (TuRFR)
TuRFR Capabilities
  2700F Gas Path
  1300F Coolant Path
  Match engine Mach and Temperature
  Optical access
    IR for surface temperatures
Propane Combustor
NGV Housing and Exhaust

## Slide 28: PHASE 3: Test Conditions
Condition | Parameter | Value
Inlet |  | 
Exit |  | 
Leading edge | (, ) | 
Trailing edge | (, ) | 
Suction surface |  | 
Condition | Parameter | Value
Inlet |  | 
Exit |  | 
Leading edge |  | 
Trailing edge |  | 
Suction surface |  | 
Nozzle box instrumentation
Raw image
Suction surface
Leading edge

## Slide 29
Leading Edge Cooling
The hub pressure ratios were varied from PRhub = 1.1-1.4 while the case pressure ratio was kept constant (PRcase = 1.15).
The contours show normalized IR signal.
Qualitatively, the signal intensity seems to drop with increasing pressure ratio at the leading edge which indicates the drop in wall temperature.
Since the case side pressure was kept constant, no significant change in signal intensity was observed.
Leading edge
section
Raw IR Image (uncooled)
Coolant feed
direction

## Slide 30
The case pressure ratios were varied from PRcase = 1.1-1.2 while the hub pressure ratio was kept constant (PRhub = 1.1).
A significant change in signal intensity was observed.
The double-walled triangular pin-fin configuration showed much more uniform signal intensity comparted to the single-walled cylindrical pin-fin which is indicative of uniform cooling.
Trailing Edge Cooling
Trailing edge
section
Coolant feed
direction
Local
hot spot
Raw IR Image (uncooled)

## Slide 31
Suction Surface Cooling
Raw IR Image
SJ-hole
777-shaped hole
Tests were performed at two pressure ratios (PRhub = 1.3,1.4) while the case side pressure ratio was kept constant (PRcase = 1.15).
The current camera location did not provide much information near the SJ hole exit.
The oxidation due to coolant injection provided an indication of the coolant trace.
The coolant trace indicates that coolant distribution is much more uniform for the SJ hole.

## Slide 32
Questions?
Applause 
Questions?

## Slide 33
List of publication
Hossain, M.A., Agricola, L.M., Ameri, A., Gregory, J., Bons, J.P., "Sweeping jet film cooling on a turbine vane," ASME. J. Turbomach. 2019;141(3):031007-031007-11. doi:10.1115/1.4042070.
Hossain, M.A., Agricola, L.M., Ameri, A., Gregory, J., Bons, J.P.,"Sweeping jet impingement cooling on a simulated turbine vane leading edge,"GPPS2018-0148, Global power and propulsion journal, 2:402-414.
Hossain, M.A., Prenter, R., Lundgreen, L.M., Ameri, A., Gregory, J., Bons, J.P., 2017 " Experimental and numerical investigation of sweeping jet film cooling," ASME J Turbomach, 140(3), p.031009
Hossain, M.A., Ameri, A., Gregory, J., Bons, J.P., "Sweeping jet film cooling at high blowing ratio on a turbine vane," ASME. J. Turbomach., 2019; Paper number: GT2019-91696 (Recommended)
Hossain, M.A., Asar, M.E., Gregory, J., Bons, J.P., "Experimental Investigation of Sweeping jet film cooling in a transonic turbine cascade," ASME. J. Turbomach., 2019; Paper number: 2019-91678 (Recommended)
Journal Publication
Patent Application
Hossain, M.A., Ameri, A., Gregory, J., Bons, J.P., " Out-of-plane Curved Fluidic Actuator," 62/854067, May, 2019 (Submitted)
Hossain, M.A., Ameri, A., Gregory, J., Bons, J.P., "Effects of Rotation on a Fluidic Actuator", AIAA Scitech 2019 Forum, AIAA SciTech Forum, AIAA 2019-0885
Hossain, M.A., Agricola, L.M., Ameri, A., Gregory, J., Bons, J.P., "Effects of Exit Fan Angle on the Heat Transfer Performance of Sweeping Jet Impingement," AIAA Propulsion and Energy Forum 2018, Ohio. (AIAA 2018-4886)
Hossain, M.A., Agricola, L.M., Ameri, A., Gregory, J., Bons, J.P., "Effects of Curvature on the Performance of Sweeping Jet Impingement Heat Transfer," 55th AIAA Aerospace Sciences Meeting, 2018, Florida
Hossain, M.A., Prenter, R., Lundgreen, R.K., Agricola, L.M., Ameri, A., Gregory, J., Bons, J.P., "Effect of roughness on the performance of Fluidic oscillator," 55th AIAA Aerospace Sciences Meeting, 2017, Texas. Paper number: AIAA 2017-0770.
Conference Publication

## Slide 34
List of publication
Hossain, M.A., Prenter, R., Lundgreen, R.K., Agricola, L.M., Ameri, A., Gregory, J., Bons, J.P., "Investigation of crossflow interaction of an oscillating jet," AIAA Aerospace Sciences Meeting,2017, Texas. Paper: AIAA 2017-1690
Agricola, L.M., Hossain, M.A., Ameri, A., Gregory, J., Bons, J.P., "Impinging Sweeping Jet Heat Transfer," 53th AIAA/ASME/SAE/ASEE Joint Propulsion Conference 2017. Paper number: AIAA 2017-4974
Agricola, L.M., Hossain, M.A., Ameri, A., Gregory, J., Bons, J.P., " Turbine Vane Leading Edge Impingement Cooling with a Sweeping Jet.," ASME Turbo Expo 2018, GT2018-77073
Lundgreen, R.K., Hossain, M.A., Prenter, R., Bons, J.P., Gregory, J., Ameri, A., "Impingement heat transfer characteristics of sweeping jet," 55th AIAA Aerospace Sciences Meeting, 2017, Texas. Paper: AIAA 2017-1535
Prenter, R., Hossain, M.A., Agricola, L.M., Ameri, A., Bons, J.P., " Experimental Characterization of Reverse-Oriented Film Cooling," ASME Turbo Expo 2017, GT2017-64731
Asar, M.E., Agricola, L.M., Hossain, M.A., Bons, J.P., " An Innovative Pin Fin Design for Turbine Trailing Edge Cooling," AIAA Propulsion and Energy Forum, Cincinnati, Ohio. (AIAA 2018-4524)
Hossain, M.A., Ameri, A., Gregory, J., Bons, J.P., "Sweeping jet film cooling at high blowing ratio on a turbine vane," ASME Turbo Expo 2019; Paper number: GT2019-91696
Hossain, M.A., Asar, M.E., Gregory, J., Bons, J.P., "Experimental Investigation of Sweeping jet film cooling in a transonic turbine cascade," ASME Turbo Expo 2019; Paper number: 2019-91678
Hossain, M.A., Ameri, A., Gregory, J., Bons, J.P., "Effects of Rotation on a Fluidic Actuator at Multiple Axis of Rotation", AIAA Scitech 2020 Forum, Orlando, Florida (Under preparation)
Hossain, M.A., Asar, M.E., Ameri, A., Bons, J.P., "Conjugate Heat Transfer Study of Innovative Pin-Fin Cooling Configuration", AIAA Scitech 2020 Forum, Orlando, Florida (Under preparation)
Hossain, M.A., Ameri, A., Gregory, J., Bons, J.P., "Experimental Investigation of Innovative Cooling Schemes On An Additively Manufactured Engine Scale Turbine Nozzle Guide Vane", ASME Turbo Expo 2020, London, UK
(Under preparation)
Conference Publication (Cont..)