## Slide 1: High–temperature Low–Nox combustor concept development Timothy C. Lieuwen, Jerry Seitzman, Suresh Menon, Matthew D. Sirignano, Vedanth Nair, Benjamin Emerson, Edwin Goh, Andreas Hoffie
UTSR Research Annual project review meeting
November 6th, 2019
Orlando, FL

## Slide 2: Motivation
Gas turbine combined cycle efficiency has steadily increased to values approaching 65%
  Driven by advances in materials and cooling methods
  Simultaneous reduction in NOx emissions enabled by advanced combustion technologies
Higher flame temperatures → higher efficiencies
New combustor paradigm is needed
  Current architectures (e.g. DLN) can’t meet current emissions standards at elevated combustor temperatures
New challenge: low NOx at high flame temperatures
1

## Slide 3: Proposed approach
Thermal NO formation dependent on temperature, residence time, and O radical concentration
Approach: Axial Staging
  Reduce residence time @ high temperatures
  Incorporate advantages of EGR (reduced [O])
Reactor model studies have demonstrated advantages and potential pitfalls of axial staging (Ahrens et al., 2016 & Goh et al, 2017)
  Highly sensitive to degree of mixing
(Bowman, 1992)
2

## Slide 4: Key research questions
(1) For a given firing temperature and residence time, what are the minimum theoretical NOx limits?
  How much lower is this fundamental limit than the limits achievable with current architectures?
(2) What do the actual fuel and air distribution patterns look like that attempt to achieve these theoretical values?
  Then, what are the operational behaviors of such a combustion system?
(3) What do local pre- & post-flame mixing patterns look like and how is the heat release distributed?
3
Notes: Emphasize theoretical and what assumptions we have to make.
Talk about how this is sort of like an MDO problem.
- Multiobjective constrained optimization problem.

## Slide 5: Executive summary
Theoretical NOx floor enabled by axial staging is O(1 ppm)
Measurements show NO production can vary significantly at a fixed rise in bulk average temperature (ΔT) across the jet
Crossflow entrainment with jet material/combustion products is critical to achieving low NOx emissions
  NOx production primarily controlled by (1) stoichiometry of the jet and (2) lift-off of the flame from the jet exit
  Vortical structures (shear layer, CVP) strongly influenced by flame lifting and shear/density layer offsets
4

## Slide 6: Top level methodology
Multi-pronged investigation with high degree of collaboration
  Reactor modeling with theoretical and practical considerations as well as optimization
  Experimental RJICF NOx emissions characterization with flame imaging
  RJICF simulation using LES
Results from each facet of investigation utilized to assist in interpreting results and informing next steps of the others
Reactor Modeling & Optimization
Detailed Simulation
Experimental Investigation
5

## Slide 7: Tools: modeling, experimental, and simulation

## Slide 8: Reactor Network models
Independent rates for mixing as well main burner product and secondary fluid entrainment: , ,
Finite mixing in reactor modeled using Interaction by Exchange with the Mean (IEM):
Secondary Fluid
Vitiated Main Burner Products
Secondary Reactor
Secondary Fluid
Non-Reacting Mixer
Vitiated Main Burner Products
Infinite mixing and entrainment
Finite mixing and entrainment
6

## Slide 9: Test Facility
Main burner & bypass air provides crossflow of lean, combustion products at a wide range of equivalence ratios
Highly configurable jet injector allows choice of diameter, velocity profile, and fuel blending
Test section with 4 sided optical access
Quench section rapidly cools exhaust to freeze NO chemistry prior to sampling
NG + Air
Bypass Air
Main Burner
Flow Conditioning
Test Section
Jet Injector
Quench Section
Residence Time Module
Emissions Sample Plane
7

## Slide 10: Diagnostics: s-PIV, Tomo-PIV, OH PLIF, OH* Chemiluminescence
Sheet Forming Optics
3” 532 nm mirror
4” diameter dichroic mirror
(reflects 284 nm, transmits 532 nm)
Tomo Slab Aperture
532 nm (tomo PIV)
Generated by GaTech Burst Mode
283 nm (OH PLIF)
Generated by GaTech Dye Laser pumped by Spectral Burst Mode
PLIF sheet now located at the center of the 532 nm slab.
Sheet Forming Optics
Jet orifice
Top window
crossflow out of page
PIV Cam 2
PIV Cam 1
PIV Cam 3
PIV Cam 4
OH
PLIF
Cam
OH*
Chemi
Cam
A
A
B
B
crossflow
Jet orifice
8

## Slide 11: Large Eddy SImulations
LESLIE simulation with AMR-CutCell1 method employed to reduce cost
Flame is resolved with 3 – 4 LES cells
Physical flow-through time of (mean)
1Muralidharan, B. and Menon, S. JCP (321), 342-368, 2016
no-slip walls
Vitiated Crossflow
Outflow
Jet
Simulation time:
  24 hrs (512 cores) for 3-species cold flow
  hrs (800 cores) for 19-species reacting flow
  flow-through times (21 days) to complete one case
10

## Slide 12: Reduced Order Modeling

## Slide 13: Key research questions
(1) For a given firing temperature and residence time, what are the minimum theoretical NOx limits?
  How much lower is this fundamental limit than the limits achievable with current architectures?
11
Notes: Emphasize theoretical and what assumptions we have to make.
Talk about how this is sort of like an MDO problem.
- Multiobjective constrained optimization problem.

## Slide 14: Modeling: Theoretical Nox minimum
Infinitely fast mixing
Constraints:
  CO constraint: 125% of Equilibrium
  Residence time
General rule for NO floor:
  Main burner as lean as possible with remainder of fuel injected as late as possible
  Minimum NO levels insensitive to global
AFS Theoretical Limit
LPM – 10 ms
NOx floor at high flame temperatures O(1ppm) !!
12

## Slide 15: Detailed investigation of local mixing and heat release

## Slide 16: Key research questions
(3) What do local pre- & post-flame mixing patterns look like and how is the heat release distributed?
17
Notes: Emphasize theoretical and what assumptions we have to make.
Talk about how this is sort of like an MDO problem.
- Multiobjective constrained optimization problem.

## Slide 17: RJICF: Flame Attachment
Leeward Attached
Lee Stabilized
(Wagner et al, 2015)
Fully Lifted
18
Simulations conducted to investigate local structure of RJICF under a variety of attachment conditions
ɸjet = 1.1
Leeward attached achieved with adiabatic wall boundary condition
Lee stabilized achieved with isothermal boundary condition
Fully lifted achieved by additionally doubling ɸjet

## Slide 18: Simulation: Attached vs Lee-Stabilized
y/D=0.8
y/D=0.8
Attached
Lee-Stabilized
20

## Slide 19: Simulation: Attached vs Lee-Stabilized
y/D=0.8
y/D=0.8
Attached
Lee-Stabilized
21

## Slide 20: Simulation: Lee-Stabilized Vs Lifted
y/D=0.8
y/D=0.8
Lee-Stabilized
Lifted
22

## Slide 21: Nox Measurements and Dependencies

## Slide 22: Key research questions
(2) What do the actual fuel and air distribution patterns look like that attempt to achieve these theoretical values?
  Then, what are the operational behaviors of such a combustion system?
23
Notes: Emphasize theoretical and what assumptions we have to make.
Talk about how this is sort of like an MDO problem.
- Multiobjective constrained optimization problem.

## Slide 23: Motivating data: Nox varies significantly at a given DT
ΔNOx as a function for constant
crossflow conditions at
ΔNOx can vary up to 3x at constant Δϕ/DT
25

## Slide 24: Motivating Data: Sensitivity to 𝜙𝑗𝑒𝑡
27

## Slide 25: Decoupling mixing, stoichiometry, and flame lifting Effects Experimental Design Approach
 | Data from pipe exit geometry
 | Data from nozzle exit geometry
 | Data from pipe exit geometry with J = 40
 | Data from methane doped pipe exit geometry
 | ϕXF = 0.45
 | ϕXF = 0.50
8
Jet parameter space at constant ΔT
  Two head end temperatures
  : Both rich and lean jets
  J: Both convectively unstable (J > 10) and globally unstable (J < 10) JICF behavior
Isolate liftoff impact
  Ethane/methane variation
Near field mixing rates
  Two approach flow boundary layer thicknesses

## Slide 26: Flame lifting
26

## Slide 27: Flame lifting
26
Lee-Stabilized

## Slide 28: Flame lifting
26
“Lean Lifted”
Lee-Stabilized

## Slide 29: Flame lifting
26
“Lean Lifted”
“Rich Lifted”
Lee-Stabilized

## Slide 30: Flame lifting
26

## Slide 31: Flame lifting
26
Increased (and thus temperature):
  Reduces lift-off distances in fully lifted flames

## Slide 32: EmissionS Normalization APproach
27
  Normalized NOx metric to collapse ∆T effect

## Slide 33: EmissionS: Sensitivity to 𝜙𝑗𝑒𝑡
27
Dependence on ∆T
  Normalized NOx metric to collapse ∆T effect
Emission data indicates two invariant results:

## Slide 34: EmissionS: Sensitivity to 𝜙𝑗𝑒𝑡
27
Dependence on ∆T
  Normalized NOx metric to collapse ∆T effect
Emission data indicates two invariant results:
  High NOx production

## Slide 35: EmissionS: Sensitivity to 𝜙𝑗𝑒𝑡
27
Dependence on ∆T
  Normalized NOx metric to collapse ∆T effect
Emission data indicates two invariant results:
  High NOx production
  Low NOx production

## Slide 36: EmissionS: Sensitivity to 𝜙𝑗𝑒𝑡
27
Dependence on ∆T
  Normalized NOx metric to collapse ∆T effect
Emission data indicates two invariant results:
  High NOx production
  Low NOx production
  LO is varying with in these cases

## Slide 37: EmissionS: Sensitivity to 𝜙𝑗𝑒𝑡
27
Dependence on ∆T
  Normalized NOx metric to collapse ∆T effect
Emission data indicates two invariant results:
  High NOx production
  Low NOx production
  LO is varying with in these cases
Region of NOx dependency upon

## Slide 38: EmissionS: Sensitivity to 𝜙𝑗𝑒𝑡
27
Dependence on ∆T
  Normalized NOx metric to collapse ∆T effect
Emission data indicates two invariant results:
  High NOx production
  Low NOx production
  LO is varying with in these cases
Region of NOx dependency upon
  NOx ↑ with ↑

## Slide 39: EmissionS: Sensitivity to LO
Emissions solutions can be associated with three lifting regimes
High NOx Production in rich lifted flames
  is varying with LO in these cases
Low NOx Production in lean lifted flames
  is varying with LO in these cases
Range of NOx in lee-stabilized flames
28

## Slide 40: EmissionS: Sensitivity to LO – Forced Lifting
29

## Slide 41: EmissionS: Sensitivity to LO – Forced Lifting
29
J = 40 points always lifted

## Slide 42: EmissionS: Sensitivity to LO – Forced Lifting
29
J = 40 points always lifted
Select series doped with methane to force liftoff

## Slide 43: EmissionS: Sensitivity to LO – Forced Lifting
29
J = 40 points always lifted
Select series doped with methane to force liftoff

## Slide 44: EmissionS: Sensitivity to J
29
J = 40 points always lifted
Select series doped with methane to force liftoff
Across all instances at fixed : NOx ↓

## Slide 45: EmissionS: Sensitivity to LO
29
Comparing methane doped point pairs (same J, fjet, DT)

## Slide 46: EmissionS: Sensitivity to LO
29
Comparing methane doped point pairs
  Monotonic reduction in NOx for increase in LO
  90% reduction in NOx achievable
  Forcing flames from lee-stabilized to “lean lifted” behavior

## Slide 47: EmissionS: Sensitivity to LO
29
NOx sensitivity to LO for fixed
Across all instances at fixed : NOx ↓
Comparing methane doped point pairs
  Monotonic reduction in NOx for increase in LO
  90% reduction in NOx achievable
  Forcing flames from lee-stabilized to “lean lifted” behavior

## Slide 48: EmissionS: Sensitivity to Exit velocity profile
30
The nozzle geometry creates a more uniform exit velocity profile than that generated by the pipe
Thinner boundary layers → larger velocity gradient → more shear
Nozzle generates more rapid onset and growth of Shear Layer Vortices (SLV)
More rapid SLV growth → enhanced near field mixing
(Gervorkyan et al., 2016)
(New et al., 2006)

## Slide 49: EmissionS: Sensitivity to Exit velocity profile
NOx reduction experienced by all of these points
  Nozzle associated with faster SLV growth rates → faster mixing (New et al, 2006)
  Mixing rate would impact post-flame dilution → lower NOx
  Mixing rate could be impacting local
NOx reduction dependent on
  Plateaus above = 4.5
30

## Slide 50: Experimental Summary
31
At constant Δφ/ΔT, NO production in RJICF can vary significantly
Three different regimes observed for NOx emissions when sweeping fjet
  High NOx production -rich lifted flames
  High NOx production, but varying with - lee-stabilized
  Low NOx production - lean lifted flames
Strong NOx dependence on LO for fixed demonstrated with forced lifting
NOx dependence on exit velocity profile at constant & J
Suggests equivalence ratio of combustion as 1st order parameter for RJICF NOx production with:

## Slide 51: Measurements: Near Field TOPOLOGY and Vortex Structure Development

## Slide 52: Tomographic RJICF experiments - SETUP
32
TPIV slab (532 nm))
OH-PLIF sheet (283 nm)
Nozzle
Crossflow
Jet
Tomographic PIV – 10 kHz (1 -4.)
Simultaneous OH-PLIF – 10 kHz (5.)
Simultaneous OH* Chemiluminescence – 10 kHz (6.)
Manufactured specialized glass piece with machined nozzle to minimize reflections
TPIV volumetric illumination spanning 60mm (length) by 8 mm (width) - OH-PLIF sheet at center of region
1.
2.
3.
4.
5.
6.

## Slide 53: TOMOGRAPHIC RJICF EXPERIMENTS – PRELIMINARY VELOCITY RESULTS
Jet
Crossflow
Jet core visualized using iso-surface
Coherent shear layer structures visualized using iso-surfaces based on Q-criterion
Windward (red) and lee (blue) structures differentiated based on out of plane vorticity

## Slide 54: FLAME LIFTING EFFECTS ON GROWTH RATES
Lifted H2-flame
Attached H2-flame
Flame lifting appears to have two effects:
(1) longer mixing times
(2) Faster mixing times

## Slide 55: MANIPULATING THE FLAME-SHEAR LAYER OFFSET
NR-Mie scattering Data
Strong SLV formation along the shear layer – visible vortex cores
Non Reacting JICF

## Slide 56: Reacting JICF Case
R – JICF
Suppressed SLV formation along the near field shear layer
Reacting JICF
NR

## Slide 57: Another Reacting JICF Case
Reacting JICF –inverted flame
R -Outer
NR

## Slide 58: Closing Summary

## Slide 59: summary
Axial staging has great potential due to a theoretical NOx floor of O(1 ppm) at high flame temperatures (>1975K)
Entrainment rate, specifically of main burner products, is critical parameter for successful axial staging implementation
  Single RJICF does not rate well against this criteria → other configurations necessary
Practical NO levels are highly sensitive to controlling parameters
Regardless of specific configuration, lifting of RJICF flames from jet exit is critical in enabling the necessary entrainment and mixing to reduce NOx
RJICF flames tend to establish themselves near stoichiometric equivalence ratios, creating hot spots
37

## Slide 60: Questions?

## Slide 61: Backup

## Slide 62: EmissionS: Equivalence ratio of combustion
20
Distinctly different profiles of based on lifting behavior

## Slide 63: EmissionS: Equivalence ratio of combustion
Equilibrium NO production rate determine by integrating over flame edge and time averaging
21

## Slide 64: EmissionS: Equivalence ratio of combustion
Equilibrium NO production rate determine by integrating over flame edge and time averaging
Forced lifting shows NOx ↓ with d[NO]/dt ↓
  Indicating forced lifting → ↓ → NOx ↓
  Exceptions observed: NOx ↓ with d[NO]/dt ↑
21

## Slide 65: EmissionS: Equivalence ratio of combustion
Equilibrium NO production rate determine by integrating over flame edge and time averaging
Forced lifting shows NOx ↓ with d[NO]/dt ↓
  Indicating forced lifting → ↓ → NOx ↓
  Exceptions observed: NOx ↓ with d[NO]/dt ↑
Change in exit velocity profile shows NOx ↓ with d[NO]/dt ↓
  Indicating reduced shear layer thickness / higher SLV growth → ↓ despite reduced lifting
21

## Slide 66: EmissionS: Equivalence ratio of combustion
Equilibrium NO production rate determine by integrating over flame edge and time averaging
Forced lifting shows NOx ↓ with d[NO]/dt ↓
  Indicating forced lifting → ↓ → NOx ↓
  Exceptions observed: NOx ↓ with d[NO]/dt ↑
Change in exit velocity profile shows NOx ↓ with d[NO]/dt ↓
  Indicating reduced shear layer thickness / higher SLV growth → ↓ despite reduced lifting
Overall data supports average as 1st order parameter
Additional effects clearly remain significant
21

## Slide 67: EmissionS: Equivalence ratio of combustion
Equilibrium NO production rate determine by integrating over flame edge and time averaging
Forced lifting shows NOx ↓ with d[NO]/dt ↓
  Indicating forced lifting → ↓ → NOx ↓
  Exceptions observed: NOx ↓ with d[NO]/dt ↑
Change in exit velocity profile shows NOx ↓ with d[NO]/dt ↓
  Indicating reduced shear layer thickness / higher SLV growth → ↓ despite reduced lifting
Overall data supports average as 1st order parameter
Additional effects clearly remain significant
A good indicator of high or low NOx
21

## Slide 68: Summary
22
At constant Δφ/ΔT, NO production in RJICF can vary significantly
Three solution paradigm observed for NOx emissions
  High NOx production associated with rich lifted flames
  High NOx production dependent on associated with lee-stabilized
  Low NOx production associated with lean lifted flames
Strong NOx dependence on LO for fixed demonstrated with forced lifting
NOx dependence on exit velocity profile at constant & J
Suggests equivalence ratio of combustion as 1st order parameter for RJICF NOx production with:
Equilibrium NO production rates from Mie scattering consistent with idea that average is a 1st order parameter for NOx production but also demonstrates significance of additional effects (e.g. variable post-flame dilution rates, intermittency of NO production, etc.)