## Slide 1: Advanced Model Development for Large Eddy Simulation of Oxy-Combustion and Supercritical CO2 Power Cycles
Joe Oefelein,a Adam Steinberg,a Devesh Ranjan,b Jacob Delimontc
aDaniel Guggenheim School of Aerospace Engineering
bGeorge W. Woodruff School of Mechanical Engineering
Georgia Institute of Technology, Atlanta, GA 30332
cPropulsion and Energy Machinery Technologies
Southwest Research Institute, San Antonio, TX 78238
DE-FOA-0001993 UTSR Project Review Meeting, Project FE0031772, November 5-7, 2019

## Slide 2: Objective … Enable detailed predictions and analysis of direct sCO2 power cycles
Technical Challenges:
  sCO2 cycles rely on a high degree of recuperation compared to traditional Rankine or open Brayton cycles, which results in high combustor inlet temperatures
  Large variation in density of inflowing CO2 occurs between the start-up and design point conditions, which results in high CO2 concentrations in high-pressure environments
  Multiphysics models must handle these atypical conditions to optimize cycle performance
Approach:
  Multiphysics model development for LES (Oefelein)
    Massively-parallel solver designed to treat high-pressure, high-temperature processes inherent to oxy-fueled combustion in complex geometries (1500 K, 30 MPa turbine inlet conditions)
  Combination of laser and optical measurement techniques for model validation applied in two complementary sCO2 configurations (Steinberg/Ranjan/Delimont)
    Quantitative density distributions using 2D burst-mode Raman scattering in sCO2 loop at G. Tech
    Chemiluminescence imaging of H2O and post-flame CO2 in the 1 MW sCO2 combustor at SwRI

## Slide 3: Modeling challenges
Physics of interest involves strongly coupled multiscale/multiphysics phenomena
  High-Reynolds-number turbulence and multiscalar mixing processes (Re > 100,000)
  High-pressure multiregime combustion and thermophysical properties
  Compressible, acoustically active flow
  Complex fuels, multiphase flow
  Complex geometries
No one research approach gives all of the information required for model development and validation
  Simulations only treat limited ranges of scales
  Experiments provide limited information
  Many sources of uncertainty
  Costs can be prohibitive
Consequence … easy to identify problems, difficult to derive improvements
Goals: 1) Mitigate challenges through synergistic combination of computational and experimental research, 2) maximize benefits of high performance computing

## Slide 4: Long term collaborations with Oak Ridge National Laboratory are enabling unique calculations
500-fold
improvement
in 9 years
OLCF-5
OLCF-4
~1 EF
200PF
27 PF
2012 Cray XK7 Titan
2021 Frontier
2018 IBM Summit
DOE Innovative and Novel Computational Impact on Theory and Experiment (INCITE) program aimed at Turbulent Scalar-Mixing and Combustion in Supercritical Fluids

## Slide 5: Theoretical – Numerical Framework (RAPTOR)
Theoretical framework (Comprehensive)
  Fully-coupled, compressible conservation equations
  Nonideal gas/liquid equation of state (high-pressure phenomena)
  Detailed thermodynamics, transport and chemistry
  Multiphase flow, spray (Lagrangian-Eulerian formulation)
  Dynamic subfilter modeling. (no tuned constants)
Numerical framework (High-quality)
  Staggered finite-volume differencing (non-dissipative, discretely conservative)
  Dual-time stepping with generalized preconditioning (all-Mach-number)
  Detailed treatment of geometry, wall phenomena, transient BC’s
Massively-parallel (Highly-scalable)
  Hybrid-parallel model for advanced many-core systems with accelerators
Results from scaling studies in July 2019 on ORNL Summit platform … demonstrated 50x speedup relative to Titan

## Slide 6: Theoretical – Numerical Framework (RAPTOR)
Theoretical framework (Comprehensive)
  Fully-coupled, compressible conservation equations
  Nonideal gas/liquid equation of state (high-pressure phenomena)
  Detailed thermodynamics, transport and chemistry
  Multiphase flow, spray (Lagrangian-Eulerian formulation)
  Dynamic subfilter modeling. (no tuned constants)
Numerical framework (High-quality)
  Staggered finite-volume differencing (non-dissipative, discretely conservative)
  Dual-time stepping with generalized preconditioning (all-Mach-number)
  Detailed treatment of geometry, wall phenomena, transient BC’s
Massively-parallel (Highly-scalable)
  Hybrid-parallel model for advanced many-core systems with accelerators
Liquid atomization, spray formation
Secondary breakup, two-way coupling
Multicomponent drop vaporization
High-pressure thermodynamics, transport
Real-fluid gas/liquid equations of state
Supercritical, multicomponent mixtures
Turbulent fluid dynamics and scalar mixing
Transient boundary conditions
Compressible, all-Mach-number flow
Multiscalar advection and diffusion
Turbulence-chemistry interactions
Complex fuels, multi-regime combustion
High-pressure chemistry, emissions, soot
Detailed and skeletal mechanisms
Optimized modeled mechanisms
Heat transfer, boundary layer dynamics
Turbulence-radiation interactions
Transient wall-flow interactions
Major focal points

## Slide 7: Detailed treatment of multicomponent mixture properties
Numerical formulation designed to handle any arbitrary set of state equations
Real-fluid gas-liquid mixture properties obtained using Extended Corresponding States model
Multicomponent formulation using cubic or BWR equations of state
Generalized to treat wide range of hydrocarbon-product mixtures (Fuel/Oxidizer/Products)
Validated via NIST, designed to run efficiently on HPC platforms across relevant regimes
Critical Point
(658 K, 18.2 bar)
n-Dodecane

## Slide 8: Hierarchy of non-reacting and reacting unit physics cases performed over a range of resolutions (DNS – LES)
Liquid Oxygen

## Slide 9: Confidence in solutions have been reinforced using different codes (here RAPTOR and CERFACS AVBP code)
AVBP
RAPTOR

## Slide 10: Both solvers produce similar results consistently over relevant ranges of conditions

## Slide 11: Currently running DNS of methane-oxygen mixing layer at device relevant conditions on Summit
DNS of 3D methane/LOX mixing layer dynamics providing unique data for understanding and modeling liquid-vapor interfacial dynamics, and treatment of nonlinearities associated with real-fluid EOS’s
Vorticity and Mixture Fraction
Scalar-Dissipation Field

## Slide 12: Characterization of turbulent inflow conditions in complex geometries
Co-Flowing
Nitrogen
Pressure | 1 bar
Temperature | 300 K
Fuel/Oxidizer Flow Rate | 85 SLM
Annular Nitrogen Flow Rate | 55 SLM
Grid Spacing | d/30, d/45, d/60
Cells Per Nozzle | 10M, 40M, 120M
Nitrogen
Shrouds
Honeycombs
Fuel (CH4/N2)
Oxidizer (O2)
Turbulence
Generator Plate
113 mm
94 mm
Co-Flowing
Nitrogen
 Low Turbulence (Ret = 600)
 High Turbulence (Ret = 1000)
Nozzle Diameter
12.7 mm

## Slide 13: Characterization of turbulent inflow conditions in complex geometries
Co-Flowing
Nitrogen
Pressure | 1 bar
Temperature | 300 K
Fuel/Oxidizer Flow Rate | 85 SLM
Annular Nitrogen Flow Rate | 55 SLM
Grid Spacing | d/30, d/45, d/60
Cells Per Nozzle | 10M, 40M, 120M
Nitrogen
Shrouds
Honeycombs
Fuel (CH4/N2)
Oxidizer (O2)
Turbulence
Generator Plate
113 mm
94 mm
Co-Flowing
Nitrogen
 Low Turbulence (Ret = 600)
 High Turbulence (Ret = 1000)
Nozzle Diameter
12.7 mm
r/d
r/d
Mean Velocity (m/s)
RMS Velocity (m/s)
Demonstrated good agreement with velocity measurements at nozzle exits by simply changing position of turbulence generator plate
Time-evolving turbulent boundary layer dynamics reconstructed using Synthetic Eddy Method (Jarrin et al., 2008)
Uses assumed, measured, or calculated turbulence properties as input (i.e., integral scale distribution, Reynolds stress tensor, and mean velocity profile)

## Slide 14: Synergistic coupling of simulations and experiments provides unique insights; e.g., Spray-A experiment
Sandia high-pressure combustion vessel (Pickett et al.)
n-Dodecane – Air
Injection and Initial Conditions
Fuel Temperature: 363 K
Chamber Pressure: 30, 60 bar
Chamber Temperature: 450, 900 K
Peak Velocity: 600 m/s
Peak Red: O(100,000)
Available Data
Rate of injection
Rayleigh scattering images
Schlieren movies
Liquid length versus time
Vapor length versus time

## Slide 15: Coupled treatment of complex thermophysics …
We see drops when n-Dodecane is injected at 363 K, 30 bar

## Slide 16: Coupled treatment of complex thermophysics …
We see drops when n-Dodecane is injected at 363 K, 30 bar, but not at 363 K, 60 bar

## Slide 17: Let’s focus on conditions at 60 bar assuming “transcritical” injection, mixing, combustion
Sandia high-pressure combustion vessel (Pickett et al.)
Compressed
Liquid
Critical Point
(658, 18.2)
Ideal Gas
Supercritical
Fluid
(363, 30)
… Drops
(363, 60)
… No Drops

## Slide 18: Detailed treatment of BC’s, thermophysics, dynamic modeling, appropriate resolution provides unique insights
Pressure (± 5 bar)
Temperature
(363 – 900 K)
Liquid Core
Turbulent Flow Structures
500 m/s (yellow) – 50 m/s (blue)

## Slide 19: Good agreement with available data using no adjustable parameters except resolution and BC’s
Jet Spreading Angle: 7.1° ± 0.8°
LES
Jet Penetration

## Slide 20: Results reveal transient mixture state just prior to autoignition
Autoignition most likely to occur where
Ignition delay time
Scalar dissipation rate
Strain rate
are simultaneously minimized
Skeen et al., PCI, 2014
Cool-flame ignition
Hot ignition
Flow just prior autoigniton
Ignition Delay
Strain Rate
Scalar Dissipation
Pressure: 60±5 bar
Equivalence Ratio (0.5 < Φ < 4)
Temperature, K (700 < T < 900)
Identification of flammable regions quantifies range of conditions where chemical mechanism must be accurate
  Temperature, K (700 < T < 900)
  Equivalence Ratio (0.5 < Φ < 4)
  Pressure: 60±5 bar

## Slide 21: Selection of candidate mechanisms presents interesting questions
Sarathy et al., 2011
  2-methyl-alkanes and n-alkanes up to C12
  2755 species
  11173 reactions
Narayanaswami et al., 2013
  Skeletal mechanism
  255 species
  2289 reactions
Luo et al., 2014
  Skeletal mechanism
  105 species
  420 reactions
All designed for up to 20 bar, 600 – 1500 K
n-Dodecane – Air
φ = 1, p = 20 bar
There is a wide range of variability between mechanisms with no monotonic convergence in accuracy

## Slide 22: Reduced order modeling applied to design chemical “model” for specific sets of operating conditions
Reduces computational cost of finite-rate chemistry while maintaining quantified level of accuracy in key chemical properties
L. Hakim, G. Lacaze, M. Khalil, K. Sargsyan, H. Najm, and J. Oefelein. Probabilistic parameter estimation in a 2-step chemical kinetics model for n-dodecane jet autoignition. Combustion Theory and Modelling, 22:446–466, 2018.

## Slide 23: We are investigating the merits of a new combustion closure based on space-time filtering
Turbulent stresses
and fluxes
Filtered chemical
source terms

## Slide 24: We are investigating the merits of a new combustion closure based on space-time filtering
e.g., Modeled instantaneous fluctuations of fuel on centerline at 100 diameters downstream of injection
∆tLES
Time, 𝜇s
Mass Fraction
n-dodecane
Hypothesis … space-time filtering can be used to close the filtered chemical source terms directly
  Apply approximate deconvolution model with assumed scalar spectrum to calculate subfilter variance/covariance matrix
  Variance/covariance matrix used as input to generate correlated scalar fluctuations on subfilter scales in time
  Modeled instantaneous signal used to evaluate filtered chemical source terms directly
Benefits … 1) conceptually regime independent, 2) minimizes assumptions required for closure, 3) approaches correct behavior in limit of DNS (i.e., facilitates hybrid-DNS/LES approach)

## Slide 25: Modeled instantaneous fluctuations facilitate formation of ignition kernels
Volume rendered fuel mass fraction
Highlighting mixing
Volume rendered temperature
Highlighting ignition kernel development

## Slide 26: Major goal moving forward is to tightly couple simulations to key companion experiments
Schlieren images by Skeen et al., PCI, 2015
250 μs
220 μs
270 μs
300 μs
380 μs
First kernel, diameter ≈ 500 μm (too small to be optically detected)
Location: tip of the jet, off-axis
Independent kernels appear, diameter ≈ 500μm to 2mm (still very small for optical detection)
Location: tip of the jet, off-axis
Many small kernels present in the “jet edge” region, what is the impact on Schlieren?
Single flame structure with upstream independent kernels, flame expands through dilatation and autoignition
Main flame region at the jet extremity, autoignition locations observed ahead of main front

## Slide 27: Current project goals … apply same approach via two complementary experiments …
Phase 1 – Non-Reacting sCO2 Loop
Phase 2 – SwRI sCO2 Combustor
Year 1
Years 2-3
Physics + Validation Data
Physics + Validation Data

## Slide 28: Non-reacting sCO2 loop
Objectives … generate progressive set of high-quality quantitative data for validation
  Focus on fluid mechanics, heat transfer, and turbulence in vicinity of vapor dome and at supercritical flow conditions
  Investigate nuances with respect to coupled treatment of turbulence, equation of state, thermodynamics, and transport
  E.g., scalar-scalar variance/co-variance fields
Diagnostics and measurement plan …
  Raman scattering measurements of sCO2 density fields
  Manufacture new test section to investigate scalar mixing processes (e.g., heated cylinder)
  Apply new “pulse burst” laser (1 J/pulse, 532 nm, 10 kHz repetition-rate, 100 pulses per burst)
Bottom flange
Back flange
3mm slot
Current optical windows
New 3-window test section (currently in design)

## Slide 29: SwRI sCO2 combustor measurements
Ballance et al., AIAA 2017-5014
SwRI sCO2 combustor
Objectives … generate reacting flow data for model validation at relevant operating conditions
  Flame holding dynamics, anchoring location, shape and structure
  Scalar mixing, turbulence-chemistry interactions
Diagnostics and measurement plan
  Preliminary focus on spectrally-resolved imaging across UV-IR
  Perpendicular viewing angles to capture 3D distribution
  Multiple wavelengths to look at different species

## Slide 30: Major outcomes
Development of a validated LES model framework that supports oxy-combustion experiments relevant to direct cycles
Creation of a synergistic combination of computational and experimental research with substantive impact on the practical design and implementation of sCO2 power cycles
Incorporation of research results into the Southwest Research Institute internal technology development process with the goal of advancing the TRL to 3 or 4

## Slide 31
Thank You

## Slide 32: Summit is currently the fastest computer in the world

## Slide 33: Validation via NIST, custom software designed to run efficiently on HPC platforms across relevant regimes
Oxygen

## Slide 34: Both solvers produce similar results consistently over relevant ranges of conditions

## Slide 35: Statistical grid convergence easily established, but level of structural dynamics required by models not clear
Vorticity – Strain
h30
h100
h250
h500

## Slide 36: Let’s focus on conditions at 60 bar assuming “transcritical” injection, mixing, combustion
1080 d
1050 d
Sandia High-Pressure
Combustion Vessel
Spray-A injector
(n-Dodecane)
Initial Conditions
Pressure: 60 bar
Temperature: 900K
Composition: 15% O2
Injection Conditions
Peak Velocity: 600 m/s
Peak Red: 117,000
Density: 650 kg/m3
Temperature: 363 K
Computational Domain
0.09 mm

## Slide 37: Turbulent flow dynamics at nozzle exit modeled using Synthetic Eddy Method
Spray-A injector
(n-Dodecane)
Injection Conditions
Peak Velocity: 600 m/s
Peak Red: 117,000
Density: 650 kg/m3
Temperature: 363 K
0.09 mm
Synthetic Eddy Method (Jarrin et al., 2008) uses measured or calculated
  Mean velocity profile
  Integral scale distribution
  Reynolds stress tensor
Provides tractable way to specify inflow boundary conditions for anisotropic, nonequilibrium, rough wall conditions, etc.

## Slide 38: ROM/UQ applied to optimize chemical “model” for specific sets of operating conditions
Objective
  Design model for specified range of operating conditions (p, T, phi) using selected reference mechanism
  Optimize model to capture specific chemical characteristics
Approach
  Start with simplest model form; e.g., equations based on Arrhenius laws for reaction rates
  Functionalize pre-exponential factors and activation energies w.r.t. operating conditions
  Use Bayesian inference to fit the most probable surfaces over specified range of conditions